# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 19/4/17 | Time: 14:10 (YDI 838) and 14:30 (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.10 at 21.9(C |  | 0.07 at 21.8(C | *didn’t filter |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 19.5(C |  | 18.7(C |  |
| Temperature (AIR) (C |  | 27.3(C |  | 25.8(C |  |
| pH pH units | Y | 6.6 |  | 7.1 |  |
| Electrical Conductivity μS/cm | Y | 480 |  | 590 |  |
| Reactive phosphate mg / L P |  | 0.07 at 23.0(C |  | 0.15 at 21.6(C | *didn’t filter |
| Turbidity NTU |  | 30 |  | 50 |  |
| Observations |  |  |
| Weather: cloudy Rainfall: During the last 2 weeks [42.0mm] During the last week [0.2mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Muddy Stream depth: 30 cm # Stream width: 75 cm Water flowing from drains: N Litter and pollutants: bottles clothing packets paper plastic Comments: # the waterway just downstream from my sampling point is particularly obstructed by reeds etc. at present, so even though the flow was rated as “slow”, the depth (30cm) was a bit above average because of the damming effect of the vegetation [see photo] There was a lot of rubbish at the site this month, washed down (and caught) after heavy rain about 9 days ago | Estimate of flow: Low Water appearance: Muddy Stream depth: 15 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: clothing paper plastic other Comments: * normally if turbidity was over 40 I would filter the sample pre- testing for Ammonium and Phosphate, but as it now seems it’s inadvisable to filter (unless it’s done all the time) I didn’t. Consequently, I did find estimating those results using the colour wheel a bit more difficult. Other litter: rusted steel strips, bike frame, wooden boards. |