# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 31/12/2017 | Time: 2:25pm (YDI 838) and 2:40pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.04 at 22.7(C | filtered | 0.04 at 22.3(C |  |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 22.4(C |  | 20.40(C |  |
| Temperature (AIR) (C |  | 25.9(C |  | 26.2(C |  |
| pH pH units | Y | 7.4 |  | 8.1 |  |
| Electrical Conductivity μS/cm | Y | 500 |  | 590 |  |
| Reactive phosphate mg / L P |  | 0.03 at 23.3(C | filtered | 0.09 at 22.7(C |  |
| Turbidity NTU |  | 50 |  | 27 |  |
| Observations |  |  |
| Weather: sunny Rainfall: During the last week [15.6mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Medium Water appearance: Muddy Stream depth: 30cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: plastic, paper, cans Comments: Turbidity was high, so I had to filter the sample for Ammonium and Phosphate tests. Signs of previous high water levels, after heavy rains earlier in the month. Several rainbow lorikeets in the trees. The row of bushes at the edge of the Fort Knox parking area has been severely lopped. I wonder why. (see photos … 8775 and 7970) | Estimate of flow: Medium Water appearance: Clear Scummy Stream depth: 20cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: plastic, bottles, cans, other Comments: There were two pieces of white laminated wood, either having been washed down or perhaps dumped there at the site. One piece was circular (about 1.5 metres diam.). It looked like a table top, but I could see nowhere that any legs might have been attached. The other piece was similar but just a half; and no sign of the other half (see photos … 8783 and 8785) Signs of previous high water levels, after heavy rains earlier in the month. pH was a bit high. |