# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 17/10/2018 | Time: 3:30pm (YDI 838) and 3:45pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.00 at 21.1(C |  | 0.00 at 20.3(C |  |
| Dissolved Oxygen mg / L |  | - |  | 8 |  |
| Temperature (WATER) (C |  | 17.5(C |  | 17.3(C |  |
| Temperature (AIR) (C |  | 21.5(C |  | 21.5(C |  |
| pH pH units | Y | 7.5 |  | 7.6 |  |
| Electrical Conductivity μS/cm | Y | 140 |  | 150 |  |
| Reactive phosphate mg / L P |  | 0.05 at 20.0(C |  | 0.03 at 20.2(C |  |
| Turbidity NTU |  | 35 |  | 30 |  |
| Observations |  |  |
| Weather: overcast Rainfall: During the last 24hrs [13.6mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: High-Medium Water appearance: Scummy Stream depth: 40cm Stream width: 0.75 metres Water flowing from drains: N Litter and pollutants: paper plastic Comments: Flattened vegetation indicating high flow, probably in the past 24 hours (see IMG_0795 on database) Noticeable soil erosion beside the drain that enters the waterway near the roundabout at the end of Rattray Rd (see IMG_0802 on database) | Estimate of flow: High-Medium Water appearance: Scummy Stream depth: 30cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: paper plastic Comments: Not a lot of litter this time. Flattened vegetation indicating high flow, probably in the past 24 hours (see IMG_0809 on database) |