# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 14/11/2018 | Time: 2:47pm (YDI 838) and 3:05pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.01 at 22.2(C |  | 0.10 at 23.7(C |  |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 17.4(C |  | 17.3(C |  |
| Temperature (AIR) (C |  | 18.3(C |  | 18.4(C |  |
| pH pH units | Y | 7.5 |  | 7.7 |  |
| Electrical Conductivity μS/cm | Y | 450 |  | 480 |  |
| Reactive phosphate mg / L P |  | 0.07 at 21.5(C |  | 0.06 at 23.0(C |  |
| Turbidity NTU |  | 17 |  | 19 |  |
| Observations |  |  |
| Weather: overcast Rainfall: During the last week [39.4 mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: High-Medium Water appearance: Scummy Stained brown Stream depth: 30 cm Stream width: 0.75 metres Water flowing from drains: N (Circumstantial hazard and additional risks) Litter and pollutants: bottles paper plastic Comments: Tree branch in the water. Recent heavy rain had washed down a lot of leaves, twigs and debris, and flattened the growth on the banks of the waterway There was a sign somebody had stuck on a post saying “Warning!!! Snake spotted in the area” IMG_0902 | Estimate of flow: High-Medium Water appearance: Frothy Stained brown Stream depth: 30 cm Stream width: 4 metres Water flowing from drains: N (Circumstantial hazard and additional risks Litter and pollutants: paper plastic Comments: Fairly clear of rubbish compared to upstream at YDI838 (Fort Knox) There was a Hazardous Materials Response Unit truck parked at the site, but I was assured by the officers that there had been no incident affecting the waterway IMG_0913 |