# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 30/01/2019 | Time: 9:05am (YDI 838) and 9:25am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.15 at 21.9(C |  | 0.4x2 = 0.8 at 22.0(C |  |
| Dissolved Oxygen mg / L |  | - |  | 4 |  |
| Temperature (WATER) (C |  | 20.6(C |  | 21.8(C |  |
| Temperature (AIR) (C |  | 20.4(C |  | 19.5 (C |  |
| pH pH units | Y | 7.5 |  | 6.5 |  |
| Electrical Conductivity μS/cm | Y | 680 |  | 530 |  |
| Reactive phosphate mg / L P |  | 0.07 at 21.8(C |  | 0.2x2 = 0.4 at 21.6(C |  |
| Turbidity NTU |  | <9 |  | 19 |  |
| Observations |  |  |
| Weather: cloudy Rainfall: During the last week [0.4mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Clear Stream depth: 30 cm Stream width: 0.75 metres Water flowing from drains: N Litter and pollutants plastic Comments: The waterway is extremely overgrown … more than I’ve ever seen here before [IMG_1243] And one section was quite scummy [IMG_1246 and IMG_1253] | Estimate of flow: Low Water appearance: Scummy Other Stream depth: 25 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: cans paper plastic Comments: Ammonium and Phosphate were again extremely high, and the samples had to be diluted, but surprisingly this time the source of the pollution was somewhere between YDI 838 (Fort Knox) and YDI 847 Susan St) rather than upstream from YDI 838 as was the case last month. The water was fairly clear, but the turbidity reading was affected by particles in the water that looked like a suspension of decomposing vegetable matter. One area was very scummy [IMG_1258] |