# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 19/02/2020 | Time: 9:10 am (YDI 838) and 9:23am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.00 |  | 0.00 |  |
| Dissolved Oxygen mg / L |  | - |  | 8 |  |
| Temperature (WATER) (C |  | 17.6(C |  | 17.3(C |  |
| Temperature (AIR) (C |  | 16.7(C |  | 14.9(C |  |
| pH pH units | Y | 7.5 |  | 7.4 |  |
| Electrical Conductivity μS/cm | Y | 17.8 |  | 17.7 |  |
| Reactive phosphate mg / L P |  | 0.10 |  | 0.09 |  |
| Turbidity NTU |  | 40 |  | 40 |  |
| Observations |  |  |
| Weather: raining Rainfall: During the last 24hrs [48mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Flood/Overbank Water appearance: Muddy Stream depth: 90+ cm Stream width: 3 metres Water flowing from drains: Y Colour _muddy__ Odour _n/a__________ Litter and pollutants: no visible rubbish or pollutants. Flow so strong everything was being washed away. Comments: I seem to recall it’s not advisable to monitor when the waterway is in flood, but I decided to do it as a one-off as it could be interesting. It was! [IMG_93 & IMG_97] The EC reading was amazingly low at both sites. [I had calibrated the EC meter using a new standard solution] Most of the other measurements were normal/good. It was not possible to get an accurate measurement of stream depth, but it was > 90cm | Estimate of flow: Flood/Overbank Water appearance: Muddy Stream depth: too deep to measure today Stream width: 5 metres Water flowing from drains: Y/ N (uncertain) Colour __________ Odour _______________ Litter and pollutants: a pink, child’s bike; otherwise very little. Flow so strong everything was being washed away. Comments: I seem to recall it’s not advisable to monitor when the waterway is in flood, but I decided to do it as a one-off as it could be interesting. It was! IMG_2305 & IMG_2306 The EC reading was amazingly low at both sites [I had calibrated the EC meter using new std. solution] Most of the other measurements were normal/good. It was not possible to get an accurate measurement of stream depth, but it was > 90cm The North and South drains are so overgrown now that it was not possible to tell if they were flowing or not, though I suspect they must have been, at least a bit. |