# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 1/11 2016 | Time: 1:55pm (YDI 838) and 2:10pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.30 at 21.1(C | High | 0.04 at 20.8(C |  |
| Dissolved Oxygen mg / L |  | - |  | 9 |  |
| Electrical Conductivity μS/cm | Y | 1430 | High | 1400 | High |
| pH pH units | Y | 6.7 |  | 7.3 |  |
| Reactive phosphate mg / L P |  | 0.10 at 20.9(C |  | 0.08 at 20.2(C |  |
| Temperature (AIR) (C |  | 19.7(C |  | 20.1(C |  |
| Temperature (WATER) (C |  | 16.8(C |  | 15.8(C |  |
| Turbidity NTU |  | 24 |  | <9 |  |
| Observations |  |  |
| Weather: overcast Rainfall: during the last week [1.4mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: A bit scummy Foamy/frothy Stream depth: 17 cm Stream width: 0.75 metres Water flowing from drains: N Litter and pollutants: cans clothing other Comments: There were some plastic rings from a beer six-pack. EC was unusually high, even for a period of Low flow Ammonium was very high at this site today too, though not so further downstream at YDI 847, which read only 0.04. It is not unusual for my readings to be lower further downstream (I’m assuming because of some in-flow along the way) but even when tests are repeated, I do occasionally find this sort of extra-large drop in concentration between the two sites. I can’t think of a good reason why this should be. | Estimate of flow: Low Water appearance: Very scummy Foamy/frothy Stream depth: 20 cm Stream width: 2 to 5 metres Water flowing from drains: N Litter and pollutants: cans paper plastic polystyrene other Comments: There was a car tyre dumped in the water. The surface of the water was extremely scummy. EC was unusually high, even for a period of Low flow Dissolved Oxygen was high today … the best I’ve recorded at this site, I think |