# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 7/3/17 | Time: 11:20am (YDI 838) and 11:50am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.50 at 23.5(C |  | 0.80 at 23.1(C | Diluted 1:1 |
| Dissolved Oxygen mg / L |  | - |  | 4 |  |
| Temperature (WATER) (C |  | 20.0(C |  | 19.9(C |  |
| Temperature (AIR) (C |  | 24.5(C |  | 26.0(C |  |
| pH pH units | Y | 6.8 |  | 6.7 |  |
| Electrical Conductivity μS/cm | Y | 800 |  | 1100 |  |
| Reactive phosphate mg / L P |  | 0.07 at 23.1(C |  | 0.40 at 22.9(C | Diluted 1:1 |
| Turbidity NTU |  | 14 |  | 14 |  |
| Observations |  |  |
| Weather: sunny Rainfall: 15 days ago [ 5.2 mm] During the last week [ 0 mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Clear Scummy Stream depth: 18 cm (“other”) Stream width: 75 cm Water flowing from drains: N Litter and pollutants: paper Comments: The site was relatively clear of litter this visit. EC was a bit high, possibly because of low flow and lack of recent rainfall. Ammonium was also high (0.50 mg/L) There have been several groundwater monitoring wells installed here recently (see photos). I’m assuming this is connected with the fact that this area is listed on the Priority Site Register, having been issued with a Clean Up Notice I saw some fish in one of the deeper, slower flowing sections, at least a dozen of them. I was able to take a small video, and some not-very-clear photos of them. They were about 6cm long; I don’t know what species. | Estimate of flow: Low Water appearance: Clear Scummy Stream depth: 15cm (“other”) Stream width: 4 metres Water flowing from drains: N Litter and pollutants: paper quite a lot of plastic other Comments: Litter included quite a lot of plastic; also a bike frame EC was high and DO was low, probably consistent with the low flow and lack of recent rainfall, although the EC reading was quite a bit higher than upstream at the Fort Knox site. Ammonium (0.80 mg/L) and Phosphate (0.40 mg/L) were particularly high this time, requiring 1:1 dilution to get readings. Comparison with the upstream site at Fort Knox was interesting, as there the Ammonium was also high (0.50 mg/L), although the Phosphate level was fairly normal. |