# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 31/5/2017 | Time: 3:25pm (YDI 838) and 3:40pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.0 at 24.0(C | filtered | 0.0 at 21.9(C |  |
| Dissolved Oxygen mg / L |  | - |  | 9 |  |
| Temperature (WATER) (C |  | 13.3(C |  | 13.4(C |  |
| Temperature (AIR) (C |  | 13.6(C |  | 13.7(C |  |
| pH pH units | Y | 6.5 |  | 6.1 |  |
| Electrical Conductivity μS/cm | Y | 180 |  | 190 |  |
| Reactive phosphate mg / L P |  | 0.02 at 23.7(C | filtered | 0.02 at 22.5(C |  |
| Turbidity NTU |  | 50 |  | 27 |  |
| Observations |  |  |
| Weather: overcast Rainfall: During the last week [ 17.6 mm] During the last 24hrs [ 7 mm ] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Flood/Overbank Medium Water appearance: Muddy Milky Stream depth: 25 cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: paper a lot of plastic Comments: The site was quite littered today, as is usual after rain. There has been just over 17mm in the past week, in addition to the 7mm over the past 24 hours. Turbidity was high. I filtered the sample before testing Phosphate and Ammonium, the levels of which were good (ie quite low) There was no sign of the fish (either this month or last month) that I saw in March. At that time, the YDI 838 turbidity was low, whereas in April it was quite a bit higher, and even higher this month. Perhaps that could be why? (even if the higher turbidity was masking their presence, I think if there were any there I would have at least seen them breaking the surface, as they did back in March) | Estimate of flow: Flood/Overbank Medium Water appearance: Milky Stream depth: 25 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: clothing paper lots of plastic Comments: There was a floating litter trap, which had probably been attached across the waterway, but had come loose from one of its two anchorage points. It was just wedged in amongst the rocks, attached at one end only. All chem. levels were good today, except perhaps for pH which was a bit lower than usual. |