# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 11/07/2017 | Time: 14:00 (YDI 838) and 14:15 (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.15 at 22.5(C | high | 0.40 at 25.2(C | v. high |
| Dissolved Oxygen mg / L |  | - |  | 9 |  |
| Temperature (WATER) (C |  | 9.2(C |  | 9.8(C |  |
| Temperature (AIR) (C |  | 14.1(C |  | 13.7(C |  |
| pH pH units | Y | 7.3 |  | 7.7 |  |
| Electrical Conductivity μS/cm | Y | 490 |  | 580 |  |
| Reactive phosphate mg / L P |  | 0.06 at 21.1(C |  | 0.25 at 27.4(C | v. high |
| Turbidity NTU |  | < 9 |  | 35 |  |
| Observations |  |  |
| Weather: sunny Rainfall: During the last week [ 5.0mm ] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Clear Scummy Stream depth: “other” 25cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: paper plastic Comments: The water was fairly clear but the surface was a bit scummy in just a couple of areas. No sign of the fish seen a few months ago. Some landscaping was being done to the left of the entrance to the area, incl. some large native plants (see photo) Ammonium was quite high but Phosphate was similar to usual Interesting to note how much colder the water was than the air temperature. | Estimate of flow: Low Water appearance: Muddy Stream depth: “other” 10 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: bottles cans paper polystyrene waxed cardboard Comments: Several pairs of ducks flew out of from the underground section when we arrived. Perhaps they are nesting in there somewhere? The water level was particularly low (see photo) Ammonium and Phosphate were both very high. Interesting to note how much colder the water was than the air temperature. |