# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 11/10/2017 | Time: 11:55am (YDI 838) and 12:15pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.45 at 20.3(C |  | 2.0 at 22.0(C | diluted x4 |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 13.4(C |  | 12.7(C |  |
| Temperature (AIR) (C |  | 19.6(C |  | 19.8(C |  |
| pH pH units | Y | 7.4 | new meter | 7.0 | new meter |
| Electrical Conductivity μS/cm | Y | 310 |  | 420 |  |
| Reactive phosphate mg / L P |  | 0.07 at 21.1(C |  | 0.4 at 22.6(C | diluted x4 |
| Turbidity NTU |  | 35 |  | 24 |  |
| Observations |  |  |
| Weather: Overcast Rainfall: During the last week [10.2mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Scummy Milky Stream depth: 25 cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: paper plastic cans other Comments: New pH meter used as from today: an Eco Testr pH2 Ammonium was very high, but Phosphate was normal. Other litter included one shotgun cartridge, a brick, and a tennis ball. Saw a family of ducks [photo] | Estimate of flow: Low Water appearance: Milky Oily Stream depth: 10 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: paper plastic Comments: New pH meter used as from today: an Eco Testr pH2 Ammonium and Phosphate were extremely high. I had to dilute the sample x4 to get a reading in each case. A pair of ducks flew out from the “tunnel” as we arrived, presumably still roosting in there somewhere. |