# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 30/05/2018 | Time: 2:35pm (YDI 838) and 2:55pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.07 at 21.6(C |  | 0.02 at 22.7(C |  |
| Dissolved Oxygen mg / L |  | - |  | 8 |  |
| Temperature (WATER) (C |  | 12.2(C |  | 12.2(C |  |
| Temperature (AIR) (C |  | 14.7(C |  | 14.3(C |  |
| pH pH units | Y | 7.5 |  | 8.0 |  |
| Electrical Conductivity μS/cm | Y | 370 |  | 390 |  |
| Reactive phosphate mg / L P |  | 0.05 at 21.1(C |  | 0.20 at 22.0(C | high |
| Turbidity NTU |  | 17 |  | 35 |  |
| Observations |  |  |
| Weather: cloudy Rainfall: During the last 24hrs [ 2.6mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Clear Scummy Stream depth: 20 cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: cans plastic Comments: A bit scummy on the surface, but just in one confined area. Saw a couple of ducks. There was almost no rubbish, but the waterway is still almost blocked in one section by vegetation. | Estimate of flow: Low Water appearance: Oily Stream depth: 20 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: paper plastic Comments: Phosphate level was significantly higher than upstream at YDI 838 (Fort Knox) Turbidity also quite a bit higher. There was very little rubbish, but there was a noticeable oil slick in one section of the waterway. One duck on the water. |