# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 30/6/2018 | Time: 2:20pm (YDI 838) and 2:35pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.10 at 20.3(C |  | 0.04 at 21.7(C |  |
| Dissolved Oxygen mg / L |  | - |  | 7 |  |
| Temperature (WATER) (C |  | 9.8(C |  | 10.4(C |  |
| Temperature (AIR) (C |  | 12.9(C |  | 12.7(C |  |
| pH pH units | Y | 7.6 |  | 8.0 |  |
| Electrical Conductivity μS/cm | Y | 650 |  | 670 |  |
| Reactive phosphate mg / L P |  | 0.09 at 22.6(C |  | 0.07 at 21.5(C |  |
| Turbidity NTU |  | 35 |  | 14 |  |
| Observations |  |  |
| Weather: cloudy Rainfall: During the last week [2.0mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Medium Water appearance: Muddy Stream depth: 35cm Stream width: 0.75 metres Water flowing from drains: N Litter and pollutants: plastic Comments: Results all fairly average this month, though turbidity a bit high. A lot of rubbish caught up, presumably as a result of 2 consecutive days of high rainfall in mid-June [photo 9599 uploaded to online database] | Estimate of flow: Medium Water appearance: Clear Oily Stream depth: 25cm Stream width: 2 to 5 metres Water flowing from drains: N Litter and pollutants: plastic oil Comments: Results all fairly average this month. There was a quite noticeable oil slick today [photo 9608 uploaded to online database] Quite a bit of general debris, presumably as a result of 2 consecutive days of high rainfall in mid-June |