# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 25/7/2018 | Time: 10:15am (YDI 838) and 10:35am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.02 at 23.5(C | filtered | 0.02 at 23.5(C | filtered |
| Dissolved Oxygen mg / L |  | - |  | 7 |  |
| Temperature (WATER) (C |  | 10.2(C |  | 10.3(C |  |
| Temperature (AIR) (C |  | 14.6(C |  | 14.2(C |  |
| pH pH units | Y | 7.4 |  | 6.7 |  |
| Electrical Conductivity μS/cm | Y | 200 |  | 270 |  |
| Reactive phosphate mg / L P |  | 0.02 at 24.5(C | filtered | 0.10 at 23.0(C | filtered |
| Turbidity NTU |  | 50 |  | 70 |  |
| Observations |  |  |
| Weather: sunny Rainfall: During the last 24hrs [4.6mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Medium Water appearance: Muddy Stream depth: “other” 35cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: paper plastic Comments: Fairly clear of new rubbish today, but still a lot there from last month. Turbidity was high, so filtration of the sample was necessary for Ammonium and Phosphate tests | Estimate of flow: Medium Water appearance: Muddy Foamy/frothy Stream depth: “other” 20cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: cans packets paper plastic other Comments: Turbidity was high, so filtration of the sample was necessary for Ammonium and Phosphate tests There was a foamy froth on the surface of the water coming from the underground section (see photo IMG_9658). Perhaps this was the reason for the higher Phosphate reading, and lower than usual pH? There was a car tyre in the water. |