# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 15/8/2018 | Time: 16:00 (YDI 838) and 16:20 (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.00 at 21.5 (C |  | 0.04 at 21.0(C |  |
| Dissolved Oxygen mg / L |  | - |  | 8 |  |
| Temperature (WATER) (C |  | 12.2(C |  | 11.8(C |  |
| Temperature (AIR) (C |  | 14.8(C |  | 15.2(C |  |
| pH pH units | Y | 7.1 |  | 8.1 |  |
| Electrical Conductivity μS/cm | Y | 270 |  | 240 |  |
| Reactive phosphate mg / L P |  | 0.02 at 20.6(C |  | 0.15 at 20.1(C |  |
| Turbidity NTU |  | 11 |  | 40 |  |
| Observations |  |  |
| Weather: overcast Rainfall: During the last week [12.6mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Medium Water appearance: Scummy Stream depth: “other” 28cm Stream width: “other” 0.75 metres Water flowing from drains: N (Circumstantial hazard and additional risks) Litter and pollutants: cans paper plastic Comments: Many twigs and branchlets scattered around, after the high winds A large piece of bent corrugated iron in the waterway (see photo on database) Some sections were quite scummy on the surface (see photos on database) | Estimate of flow: Medium Water appearance: Muddy Oily Stream depth: “other” 25cm Stream width: 2 to 5 metres Water flowing from drains: N (Circumstantial hazard and additional risks Litter and pollutants: paper plastic other Comments: The waterway had quite a marked oil slick today [see photo on database] Considering it was around “knock-off” time at the nearby motor mechanic businesses, I wonder if the oil might have been run-off from the end-of-day hose downs? The pH, turbidity and Phosphate readings were significantly higher here too, compared with those upstream at YDI 838 Other litter included some glass bottles, and also the car tyre which has been there in the water for a few months now. |