# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 19/12/2018 | Time: 11:30am (YDI 838) and 11:10am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.4 x4 = 1.6 at 23.2(C | diluted | 0.50 |  |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 19.9(C |  | 19.5(C |  |
| Temperature (AIR) (C |  | 24.0(C |  | 22.4(C |  |
| pH pH units | Y | 7.4 |  | 7.5 |  |
| Electrical Conductivity μS/cm | Y | 540 |  | 540 |  |
| Reactive phosphate mg / L P |  | 0.15 at 21.8(C |  | 0.20 at 21.6(C |  |
| Turbidity NTU |  | 40 |  | 15 |  |
| Observations |  |  |
| Weather: overcast Rainfall: during the last week [68mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Medium Water appearance: Muddy Stream depth: 25 cm Stream width: 0.75 metres Water flowing from drains: N Colour __________ Odour _______________ (Circumstantial hazard and additional risks) Litter and pollutants: paper plastic Comments: Ammonium level was extremely high: it was necessary to dilute the sample 1:4 to get a reading. There were new signs up in the area warning to be on the look out for snakes. | Estimate of flow: Medium Water appearance: Scummy Oily Stream depth: 20 cm Stream width: 4 metres Water flowing from drains: N Colour __________ Odour _______________ (Circumstantial hazard and additional risks Litter and pollutants: bottles oil paper plastic Comments: Ammonium level was high, but nowhere near as high as upstream at YDI838 … presumably diluted on the way down stream, as if frequently observed here. There were areas between the rocks where the surface was very scummy (see photo) Also some oil on the surface in other spots. |