# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 23/04/2019 | Time: 10:00am (YDI 838) and 10:20am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.02 at 22.2 (C |  | 0.30 at 23.9 (C |  |
| Dissolved Oxygen mg / L |  | - |  | 5 |  |
| Temperature (WATER) (C |  | 15.4 (C |  | 16.6 (C |  |
| Temperature (AIR) (C |  | 19.3 (C |  | 18.2 (C |  |
| pH pH units | Y | 6.9 |  | 4.2 |  |
| Electrical Conductivity μS/cm | Y | 360 |  | 510 |  |
| Reactive phosphate mg / L P |  | 0.10 at 22.9(C |  | 0.6 at 22.8 (C | 0.20 x 3 |
| Turbidity NTU |  | 14 |  | 17 |  |
| Observations |  |  |
| Weather: overcast Rainfall: During the last week [0.8mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Clear Stained brown Frothy Stream depth: 25 cm Stream width: 75 cm Water flowing from drains: N Litter and pollutants: bottles plastic polystyrene Comments: The waterway is still very overgrown, with sections where the water is not even visible from above. There was a large area with a lot of speckly froth on the surface, though the ducks didn’t seem to mind [IMG_1479], and there were some unidentified water bugs or small fish breaking the surface in the area too. | Estimate of flow: Low Water appearance: Scummy Oily Stream depth: 20 cm Stream width: 4 metres Water flowing from drains: N Litter and pollutants: bottles cans packets paper plastic Comments: The Ammonium reading was higher than normal, but the Phosphate was extremely high (a 1:3 dilution was required in order to obtain a reading). And the pH was abnormally low. These figures were vastly different from the readings from the Fort Knox site [YDI 838] sampled a short while earlier upstream, all of which were relatively normal. Scummy sludge caught in the rocks [IMG_1485) Oil slick on the surface near the exit from the underground section (IMG_1482] |