# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 9/7/2019 | Time: 2:50pm (YDI 838) and 3:10pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.04 at 21.8(C |  | 0.30 at 22.7(C | filtered |
| Dissolved Oxygen mg / L |  | - |  | 7 |  |
| Temperature (WATER) (C |  | 11.5(C |  | 12.4(C |  |
| Temperature (AIR) (C |  | 14.2(C |  | 14.0(C |  |
| pH pH units | Y | 7.2 |  | 7.4 |  |
| Electrical Conductivity μS/cm | Y | 440 |  | 190 |  |
| Reactive phosphate mg / L P |  | 0.15 at 21.4(C |  | 0.15 at 22.6(C | filtered |
| Turbidity NTU |  | 20 |  | 80 |  |
| Observations |  |  |
| Weather: overcast Rainfall: During the last 24hrs [1mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Medium Water appearance: a bit muddy Stream depth: “other” [30 cm] Stream width: “other” [0.75 metres] Water flowing from drains: Y Colour __muddy_ Odour _?_ (Circumstantial hazard and additional risks) Litter and pollutants: plastic other Comments: Rubbish included a plastic shopping basket. Unusually, the drain that runs underground alongside Sherbourne Rd was carrying water today; it was quite muddy-looking. The water coming along from the main drain was frothy in parts. | Estimate of flow: Medium Water appearance: Muddy Scummy Stream depth: “other” [25 cm] Stream width: “other” [4 metres] Water flowing from drains: N Colour __________ Odour _______________ (Circumstantial hazard and additional risks Litter and pollutants: bottles cans packets paper other Comments: Rubbish included a fluorescent tube, a couple of balls. The overhanging branch is still catching and retaining a lot of rubbish Turbidity was very high; I filtered the sample before testing Ammonium and Phosphate |