# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 29/10/2019 | Time: 11:10am (YDI 838) and 11:30am (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.00 at 25.5(C |  | 0.08 at 22.7(C | filtered |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 14.9(C |  | 15.3 (C |  |
| Temperature (AIR) (C |  | 26.5(C |  | 21.3(C |  |
| pH pH units | Y | 6.9 |  | 5.7 | Unusually low |
| Electrical Conductivity μS/cm | Y | 230 |  | 450 |  |
| Reactive phosphate mg / L P |  | 0.08 at 25.5(C |  | 0.05 at 23.7(C | filtered |
| Turbidity NTU |  | 30 |  | 60 |  |
| Observations |  |  |
| Weather: sunny Rainfall: During the last 24hrs [3.2mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Muddy Scummy Stream depth: “other” 30cm Stream width: 75 cm Water flowing from drains: N Colour __________ Odour _______________ (Circumstantial hazard and additional risks) Litter and pollutants: bottles paper plastic other Comments: Included in the litter were several wooden planks (building materials), and a large metal tray. Waterway was particularly overgrown with weeds etc. | Estimate of flow: Low Water appearance: Muddy Scummy Stream depth: “other” 20cm Stream width: 4 metres Water flowing from drains: N Colour __________ Odour _______________ (Circumstantial hazard and additional risks Litter and pollutants: bottles cans paper plastic Comments: pH was unusually low. Turbidity was high, and sample for Ammonium and Phosphate testing filtered |