# Physical / Chemical Analysis      Karingal Yalloc monitoring  (Leonie & Tony Morgan)

| Site Code: | YDI 847 (Karingal Yalloc) |
| --- | --- |
|  | ~20m East of Susan St, Eltham Melway ref. 21 H7 |
| Site Code: | YDI 838 (Karingal Yalloc) |
|  | near Fort Knox Self-Storage Melway ref. 21 G5 |
| Monitoring | Date: 22/01/2020 | Time: 2:20pm (YDI 838) and 2:45pm (YDI 847) |

| Parameter | calib | YDI 838 (Fort Knox) | YDI 847 (Susan Street) |
| --- | --- | --- | --- |
| Ammonium mg / L NH4+ |  | 0.0 |  | 0.0 |  |
| Dissolved Oxygen mg / L |  | - |  | 6 |  |
| Temperature (WATER) (C |  | 21.5(C |  | 20.3(C |  |
| Temperature (AIR) (C |  | 31.5(C |  | 28.0(C |  |
| pH pH units | Y | 7.4 |  | 8.6 |  |
| Electrical Conductivity μS/cm | Y | 460 |  | 480 |  |
| Reactive phosphate mg / L P |  | 0.07 |  | 0.10 |  |
| Turbidity NTU |  | 24 |  | 19 |  |
| Observations |  |  |
| Weather: overcast windy Rainfall: During the last week [ 62mm] During the last 24 hours [ 0mm] YDI 838 (Fort Knox) YDI 847 (Susan Street) |
| Estimate of flow: Low Water appearance: Muddy Scummy Stream depth: 30 cm Stream width: 50 cm Water flowing from drains: N Litter and pollutants: bottles cans paper plastic other Comments: Other litter included a large quantity of branches, twigs and leaves. There had clearly been a lot of water flowing recently as a result of the heavy rains, but because there had been no rain in the past 24 hours or so, flow had returned to low-normal. Despite this, the actual depth of the stream stays fairly constant, just reduced width. We were pleased to meet the Fort Knox Storage manager (Catherine). She came over to us to chat. They do a great job maintaining the appearance of the area, and she clearly takes quite an interest in it all. Ammonium and Phosphate levels were good today. | Estimate of flow: Low Water appearance: Muddy Stream depth: 30 cm Stream width: 2 metres Water flowing from drains: N Litter and pollutants: bottles cans packets paper plastic other Comments: Other litter included balls, a sheet of Perspex, and some small boards. Signs of heavy flow after the recent rain events, but flow was back to low-normal as there has been no rain in the past 24 hours or so. The depth of the waterway doesn’t lessen much when there is not a lot of water flowing; just the width narrows a bit. Today the air temperature down at water level was noticeably less than that at street level, as the air coming out from the underground section was very much cooler. Ammonium and Phosphate levels were good. pH slightly high. |